## Slide 1: Chapter 5 - Operational Amplifiers

## Slide 2: Outline
Operational amplifier (op amp)
Basic operations
DAC
Instrumentation amplifier

## Slide 3: The Op Amp
Behaves like a voltage-controlled voltage source with very high amplification factor
When combined with resistors, capacitors, and inductors, can perform various functions:
  amplification/scaling
  sign changing
  addition/subtraction
  integration
  differentiation
  analog filtering

## Slide 4: Op Amp Terminals
Five important terminals
  The inverting input
  The noninverting input
  The output
  The positive (+) power supply
  The negative (-) power supply
The rest three terminals
  2 Offset Null (Balance)
    May be used to compensate for performance degradation due to aging etc.
  1 No Connection (NC)
    Unused, not connected to the amplifier circuit.

## Slide 5: Output Voltage
The voltage output of an op-amp is proportional to the difference between the noninverting and inverting inputs
共模抑制比： or
Op Amp in the real world
Notes: The above formula depends on the choice for 0 V point.

## Slide 6: uA741 Functional Block Diagram

## Slide 7: Equivalent Circuit of an Op Amp
The total current into the three terminals（Vi+, Vi-, and Vo) of an amp is nonzero.
KCL can still be applied to each node, but not to the model circuit as a whole (the red box) because Vcc+ and Vcc- are not part of the model circuit.
Vcc+
Vcc-
Vi+
Vi-
Vo

## Slide 8: Voltage Saturation
Is the output voltage unlimited?
Notes: How do we know the op-amp is operating in linear region?

## Slide 9: Example 1
find vo, assuming the output
假设输出电压的工作范围为
voltage range is .

## Slide 10: Feedback
Negative feedback
voltage difference
负反馈：当输出端电压变化通过外部电路反馈至输入端时，反馈信号引起的输出端电压变化方向与原变化方向相反且通常幅度更大,从而能抵消输出电压的变化，维持输出电压稳定。
Positive feedback
voltage difference
正反馈：当输出端电压变化通过外部电路反馈至输入端时，反馈信号引起的输出端电压变化方向与原变化方向相同,从而加剧输出电压的变化。
Notes: https://en.wikipedia.org/wiki/Negative_feedback_amplifier

## Slide 11: Example 2
Find vo / vs

## Slide 12: Example 2 (solution)
注意：当时（正反馈），同样可以得到，但此时电压不稳定。

## Slide 13: Attributes of an Ideal Op Amp
  infinite open-loop gain:
  infinite input resistance:
  zero output impedance: (not necessary for applying the golden rules)

## Slide 14: Ideal Op-Amp Analysis
Property 1: Gain is infinite The potential between the op-amp input terminals, v(+) – v(-), equals zero.
R2
R1
-
+
V0
VIN
Property 2: Input resistance is infinite The currents flowing into the op-amp’s two input terminals both equal zero.
No Potential Difference
No Currents
When there exists negative feedback,
Property 1 introduces an additional equation which replaces the KCL equation at the output node.

## Slide 15: Example 3
Find vo / vs
R1
R2
Equivalent circuit
Note： there is no involvement of R0 in the analysis.

## Slide 16: Outline
Operational amplifier (op amp)
Basic operations
    sign changing
    amplification/scaling
    addition/subtraction
    integration
    differentiation
    analog filtering
DAC
Instrumentation amplifier

## Slide 17: Inverting Amplifier
Apply KCL at node -,
we have

## Slide 18: Non-inverting Amplifier
Apply KCL at node -,
we have
)
When and , we get , i.e. a voltage follower.

## Slide 19: Application: Voltage Follower
Direct connection
Equivalent Thevenin circuit:
Input side: VTh=Vs; RTh Rs, load
Output side: VTh=Vs; RTh 0, load RL
Equivalent Thevenin circuit: VTh=Vs; RTh Rs, load RL
Voltage follower
Notes:   𝑅_2=0,𝑅_1=∞
  𝑣_𝑜=𝑣_𝑖𝑛 (𝐴=1)

## Slide 20: Practice 1
Determine in the circuit shown below
Answer: (V0-2)/40=-4/20; V0 = -6 V;

## Slide 21: Practice 2
Determine in the circuit shown below.
V0/Rf=-[(is*R2)/(R1+R2)]
右边[..]内可理解为：
并联电路分流或
电源等效变换后串联电路的电流

## Slide 22: Summing Amplifier
Aside from amplification, the op-amp can be made to do addition readily.

## Slide 23: Practice
Find and in the circuit shown below
V

## Slide 24
Exercise: find the relationship between and input voltages , , and . What is the disadvantage of such a summing amplifier compared to the one in the previous slide?

## Slide 25
Answer:
However, the current into each terminal is affected by the voltages at the other input terminals, which is not desirable and should be avoided. Remember: for non-ideal voltage source, the output voltage varies with output current.

## Slide 26: Ideal Op-Amp Analysis
Property 1: Gain is infinite The potential between the op-amp input terminals, v(+) – v(-), equals zero.
R2
R1
-
+
V0
VIN
Property 2: Input resistance is infinite The currents flowing into the op-amp’s two input terminals both equal zero.
No Potential Difference
No Currents
When there exists negative feedback,
Property 1 reduces the number of unknown voltages by 1 which compensates the lack of KCL equation at the output node.

## Slide 27: Difference Amplifier

## Slide 28: Difference Amplifier (solution)
Note: current from voltage source 1 is affected by , but not the other way around.

## Slide 29: Differentiator
Find the relationship between and in the circuit shown below
For this equation to be valid, the response time of the op-amp must be much shorter than .

## Slide 30: Integrator
Find the relationship between and in the circuit shown below. What if the capacitor is replaced by a inductor?
,
If C is replaced by an inductor,
Note: both RC and have the dimension of time.
+
-

## Slide 31: Practice 3
Determine the equivalent resistance at terminals a-b.
Answer:
a
b

## Slide 32: Practice 4
a
b
Determine the Thevenin’s equivalent resistance at terminals a-b.

## Slide 33: Practice 4 (solution)
,
Vs=isR2
Open circuit
Short circuit
From ideal op-amp approximation, we have

## Slide 34: Application - DAC
Digital Input
0
1
2
3
4
5
6
7
8
Analog Output (V)
14
8
4
0
1
The voltage levels are discrete
It is proportional to the digital value
Approximately continuous if the step is small enough
2
16

## Slide 35: Binary representation
Digital value =
, or 1.
LSB
MSB

## Slide 36: DAC
）
If ， ， then =）
二进制数字的值

## Slide 37: DAC
4-Bit D/A
8V
-
+
V0
5K
80K
40K
20K
10K
S1
+ -
S3
S2
S4
-
+
“Weighted-adder D/A converter”
(Transistors are used as electronic switches)
=

## Slide 38: Instrumentation Amplifier
The amplification factor controllable and not too large to allow a sufficient dynamic range.  multiple resistance options.
The input signal often has an unknown offset  differential amplifier.
The Thevinen resistance of the input signal is not negligible.  two stage design.

## Slide 39: Instrumentation Amplifier
Ad8231
R1
R2
R3
V2
V1
The circuit can be separated into 2 stages
Stage 1:
Stage 2:
Vi-
Vi+

## Slide 40: Instrumentation Amplifier (practice 5)
下图为某仪表放大器的内部电路图，如果将端口12与3相连，端口9与10相连，端口6接地。求 OUTPUT(端口9)的电压与“+input”(端口2)- “-input” (端口1)间电压差的关系。
V1
V2

## Slide 41: practice 5 solution
Voutput=V2-V1
V+input-V-input
=(V2-V1)
Voutput=(V+input-V-input)
Voutput=200(V+input-V-input)